## Slide 1: AI-Systems Hardware For Machine Learning (294-162)
Amir Gholami & Joseph E. Gonzalez

## Slide 2: Acknowledgments
Many slides from Prof. Kurt Keutzer, Suresh Krishna, Prof. Patterson, Michael Pellauer (Nvidia), Prof. Sophia Shao, Naveen Kumar (Google), Pallas Group

## Slide 3: Agenda for Today
1:10-2:00: Preliminary Lecture on Hardware for ML
2:00-2:45: PC Meeting Discussions
2:45-3:00: Break
3:00-4:00: Guest Lecture by Dr. Reynold Xin (Databricks)

## Slide 4: Objectives For Today
Key Trends in Hardware and motivation for DSAs
Reduced Precision Training
Different DataFlow Patterns in Hardware
How to evaluate a HW with Roofline Model
Important context for papers and what to expect

## Slide 5: Key Drivers for Neural Network Success
Faster
Computation
More Complex Nets
More
Data
DARPA Neural Network Study Final Report (606 pages):
“After participating in this Study, my personal view is that neural networks will provide the next major advance in computing technology.”
Dr. Jasper Lupo
DARPA, Washington, DC
June, 1988

## Slide 6: AlexNet vs Lenet5: 1000x More Compute
1500x
Amir Gholami, Zhewei Yao, Sehoon Kim, Michael W. Mahoney, Kurt Keutzer, AI and Memory Wall, Riselab Medium Blogpost, 2021.

## Slide 7: General Purpose Hardware Trend
Key Observations
# Transistors still increasing
Single Core Performance Plateauing
End of Dennard Scaling
Distributed Computing
42 Years of Microprocessor Trend Data, Karl Rupp

## Slide 8: Common Fallacy: Moore’s Law is not Dead
Moore, Gordon E. "No exponential is forever: but ‘Forever’ can be delayed!" Solid-State Circuits Conference, 2003.
15X
Slide from Prof. Patterson

## Slide 9: It is becoming increasingly difficult to push the boundary
Building a 3nm fab costs around $20B. This is still economical given the $600B ARR for the semi-conductor industry, but it is questionable how much farther we can push the limit.
Source: high end performance packaging 3d/2.5d integration report, Yole, Development, 2020.

## Slide 10: But It has Slowed Down
Based on SPECintCPU. Source: John Hennessy and David Patterson, Computer Architecture: A Quantitative Approach, 6/e. 2018
End of the Line?
2X / 20 yrs
(3%/yr)
RISC
2X / 1.5 yrs
(52%/yr)
CISC
2X / 3.5 yrs
(22%/yr)
End of Dennard
Scaling
⇒
Multicore
2X / 3.5 yrs
(23%/yr)
Am-
dahl’s
Law
⇒
2X / 6 yrs (12%/yr)
Notes: RISC - threw computers away since too slow
Have to rethink what we’re doing

## Slide 11: Domain Specific Accelerators
John Hennessy and David Patterson, “A New Golden Age for Computer Architecture,” Communications of the ACM, February 2019

## Slide 12: Domain Specific Accelerators
2.5K – 30K X increase in MOPs/mW
25,300 MOPS/mW
11,500 MOPS/mW
140,300 MOPS/mW
~3.23 – 4 MOPS/mW (835)
11– 16.6 GFLOPS SGEMM (835)
SnapDragon 835 ( 845  855)

## Slide 13
basicmi.github.io/AI-chip

## Slide 14: Two Important Innovations in AI Hardware That We Will Cover Today
Low Precision Arithmetic Units
Custom DataFlow Design

## Slide 15: Low Precision Training

## Slide 16: Low Precision Training
1.21042
× 0.61127
0.73989343
about 1.2
× about 0.6
about 0.7
=>
For a lot of the operations in ML we use randomized algorithms. So why not use low precision instead of FP32 or FP64?
First, let’s see how much performance gain we can get
Second, there are subtleties associated with limited precision that need to be resolved

## Slide 17: How much is on the table with low precision?
At least 2x reduction in energy with FP16 compute

## Slide 18: How much is on the table with low precision?
At least 2x reduction in energy with FP16 compute
Significant gains in power if the parameters could be stored in SRAM vs DRAM
Memory hierarchy from Andrew Walker, EE Times.

## Slide 19: Why can’t we just increase SRAM?
SRAM is 100x more expensive than DRAM and importantly occupies more area of the chip!
Using FP16 instead of FP32/64 reduces access volume without having to incur this cost
Intel Sandy Bridge-E Processor Die (Credit Rui Pan)

## Slide 20: Faster Compute with FP16
The main reason for higher throughput is that FP16 ALUs take less area on the chip so we can pack more ALUs per unit area

## Slide 21: Lower Precision Arithmetic Requires Less Transistors -> Less Area
int4 MAC
4 bit multiply , 16 bit accumulator
~700 gates
X
+
4b
16b
4b
8b
32 bit FP fused MAC
17K gate equivalents
24 X less gates
Notes: S. Galal, “ENERGY EFFICIENT FLOATING-POINT UNIT DESIGN”,
http://www-vlsi.stanford.edu/people/alum/pdf/1211_SamehGalal_FP_Design.pdf
Randy Katz, “Arithmetic Circuits”, Part II, CS150 Lecture#24, Fall 2005
Sumant Dalmiya, “A Comparative Study of Adders “, UT MSE Report, 2015, https://repositories.lib.utexas.edu/bitstream/handle/2152/35326/DALMIYA-MASTERSREPORT-2015.pdf?sequence=1&isAllowed=y

## Slide 22: 16 Bit Representation
Float32: (range ~1e-38 to ~3e38)
Float16: (range ~5.96e-8 to 65,504)
BFloat16: (range ~1e-38 to ~3e38)
* Google largely avoided low precision training problems with BFLOAT16

## Slide 23: FP16/32 Training Workflow

## Slide 24: ML Challenges with FP16 Training
Naïve FP16 training leads to divergence/poor accuracy
FP16 has very limited dynamic range:
Max =65504 , Min Normal Number = 2−14
This creates several challenges in training NN:
Loss of precision during weight update
Exacerbates ‘‘vanishing and exploding gradients’’
Overflow/underflow for layer activations during forward/backward pass
Loss curve for training AlexNet on ImageNet
P. Micikevicius, S. Narang, J. Alben, G. Diamos, E. Elsen, D. Garcia, B. Ginsburg, M. Houston, O. Kuchaiev, G. Venkatesh, H. Wu. Mixed precision training. ICLR’18. B. Ginsburg, S. Nikolaev, A. Kiswani, H. Wu, A. Gholami, S. Kierat, M. Houston, A. Fit-Flores. Tensor processing using low precision format. US Patent 15/624577.

## Slide 25: Limitations of Floating Points
Figure Reference: volkerschatz.com
There are only a finite number of different floats
Floats are discrete but not equidistant
A hypothetical 8-bit floating point representation with 1 bit sign, 3 bit exponent, 4 bit mantisa
Notice that the representable numbers are not equidistant
Teaser question: What is the best way to sum an array with a lot of small values and some very large values to minimize numerical error?
In IEEE representation no associative property

## Slide 26: Unit in the Last Place (ULP)
Floating points can only represent specific real valued numbers
Can lead to stalling at one point if the gradients are small
a
a + 1ULP

## Slide 27: Stochastic Rounding
One popular solution proposed to avoid this stalling is stochastic rounding
a
a + 1ULP
Gupta S, Agrawal A, Gopalakrishnan K, Narayanan P. Deep learning with limited numerical precision. InInternational Conference on Machine Learning 2015 Jun 1 (pp. 1737-1746).
Ho ̈hfeld, Markus and Fahlman, Scott E. Probabilistic rounding in neural network learning with limited precision. Neurocomputing, 4(6):291–299, 1992.

## Slide 28: Stochastic Rounding
About 5 percent accuracy loss for a 3 layer CNN on Cifar-10
Gupta S, Agrawal A, Gopalakrishnan K, Narayanan P. Deep learning with limited numerical precision. In International Conference on Machine Learning 2015 Jun 1 (pp. 1737-1746).
Ho ̈hfeld, Markus and Fahlman, Scott E. Probabilistic rounding in neural network learning with limited precision. Neurocomputing, 4(6):291–299, 1992.

## Slide 29: Vanishing Gradient Problem
Main problem is in representing gradients
Solution to be discussed during next week’s PC meeting for [Micikevicius, 2018] paper!

## Slide 30: Further Reading (INT8 Training?)
Several recent papers have proposed INT8 training. The ideas are interesting but:
Many layers need to be kept at higher precision (FP16 or FP32)
Master copy of weights needed at higher precision
Lots of Hyper-parameter tuning is needed
Interesting papers to read:
Training DNNs with 8-bit FPs [NeurIPS’18]
HybridFP8 Training [NeurIPS19]
Shifted and Squeezed 8-bit Floating Point [ICLR’20]

## Slide 31: Custom DataFlow

## Slide 32: Motivation: Use A Custom DataFlow to minimize DRAM Accesses
DRAM access are 100x costlier than SRAM.
The number of times that we access DRAM depends on the order of the computations in our code!
The goal is to find an order/dataflow to minimize this cost

## Slide 33: Custom DataFlow Motivation
Minimize data fetching from DRAM
DRAM
(Weights, Inputs, Outputs)
On-Chip Buffer
Compute Core
Intel Sandy Bridge-E Processor Die (Credit Rui Pan)

## Slide 34: Taxonomy of Dataflow in NN Accelerators
Weight Stationary (WS)
A PE reuses a kernel weight across different input activations.
Examples: TPU[2], CNP[3]
[1] Y.-H. Chen, et. al., “Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks,” 2016.
[2] N. Jouppi, et al., “In-Datacenter Performance Analysis of a Tensor Processing Unit,” 2017.
[3] C. Farabet, et al., “CNP: An FPGA-based processor for Convolutional Networks,” 2009.
[4] Z. Du, et al., “ShiDianNao: Shifting vision processing closer to the sensor,” 2015.
Output Stationary (OS)
A PE accumulates partial products.
Examples: ShiDianNao (SOC-MOP)[4], Envision (MOC-MOP)[5], DNA[6]
We can classify NN accelerators based on spatial/systolic architecture according to the type of data each PE locally reuses.
[5] B. Moons, et al., “Envision: A 0.26-to-10TOPS/W subword-parallel dynamic-voltage-accuracy-frequency-scalable Convolutional Neural Network processor in 28nm FDSOI,” 2017.
[6] F. Tu, et al., “Deep Convolutional Neural Network Architecture With Reconfigurable Computation Patterns,” 2017.C

## Slide 35: Weight Stationary DataFlow (TPU)
How often are outputs/inputs accessed?
How about the weights?
Every Cycle
Every X’ Cycles

## Slide 36: What do we mean by Stationary?
The datatype (and dimension) that changes most slowly
Imprecise analogy: think of data transfers as a wave with “amplitude” and “period”
  The stationary datatype has the longest period (locally held tile changes most slowly)
  Later we will see how intermediate staging buffers reduce both bandwidth and energy
Often corresponds to datatype that is “done with” earliest without further reloads
Michael Pellauer, MICRO, 2020

## Slide 37: Impact of Local Buffer
DRAM
(Weights, Inputs, Outputs)
On-Chip Buffer
Compute Core
Buffer size be to minimize refetching data from DRAM?
Dataflow | Outputs | Inputs | Weights
Weight Stationary (WS) | X’ | X | 1
What is the energy cost of accessing the buffers?
Where f is the energy of accessing a buffer of size x. See PPT notes for derivation.
Notes: Deriving the energy cost is very simple:
For all of the loop over x (inner loop), we only need to read w[s] once. The cost of this is f(1) as the buffer size for weights is 1.
Accessing i[x+s] at every iteration requires reading the input buffer which has a size of X’. Therefore this energy cost per cycle is f(X’)
Similarly, accessing o[x] has a cost of f(X’) to read the current value stored in the buffer, and an additional f(X’) to write back the result after accumulation
The above three result in an energy cost of f(1) + f(X’) + 2f(X’). The loop has a total of SX’ iterations, hence the result in the slide.
SX’ [f(X’) + f(X') + f(X') + f(1)]

## Slide 38: Output Stationary DataFlow
Every S Cycles
Every Cycle
How often are outputs accessed?
How about weights/inputs?

## Slide 39: Impact of Local Buffer: OS
DRAM
(Weights, Inputs, Outputs)
On-Chip Buffer
Compute Core
Buffer size be to minimize refetching data from DRAM?
Dataflow | Outputs | Inputs | Weights
Output Stationary (OS) | 1 | S | S
What is the energy cost of accessing the buffers?
Where f is the energy of accessing a buffer of size x. See PPT notes for derivation.
Notes: Deriving the energy cost is very simple:
For all of the loop over s (inner loop), we only need to read o[s] once. The cost of this is f(1) as the buffer size for outputs is 1. We also need to write to this buffer and thus we will incur another f(1) cost.
Accessing i[x+s] at every iteration requires reading the input buffer which has a size of S. Therefore this energy cost per cycle is f(S)
Similarly, accessing w[s] has a cost of f(S).
SX’ [f(1) + f(1) + f(S) + f(S)]

## Slide 40: Weight Stationary vs Output Stationary
Dataflow | Outputs | Inputs | Weights
Weight Stationary (WS) | X’ | X | 1
Output Stationary (OS) | 1 | S | S
Buffer size be to minimize refetching data from DRAM
Very different energy cost of accessing the local buffers by just a change in the loop order
WS:
OS:

## Slide 41: Convolution: Restructured as Matrix Multiplication
2,0,0
2,0,1
0,0
0,1
1,0
1,1
0,2
0,3
1,2
1,3
2,0
2,1
3,0
3,1
2,2
2,3
3,2
3,3
Input
w2,0
w2,1
w2,2
Weight
Output
w1,0
w1,1
w1,2
w0,0
w0,1
w0,3
w0.4
w0,2
w0,5
w0,6
w0,7
w0,8
1,0,0
1,0,1
0,0,0
0,0,1
0,1,0
0,1,1
0,0
0,1
1,0
1,1
0,2
0,3
1,2
1,3
2,0
2,1
3,0
3,1
2,2
2,3
3,2
3,3
0,0
0,1
1,0
1,1
0,2
0,3
1,2
1,3
2,0
2,1
3,0
3,1
2,2
2,3
3,2
3,3
In practice we deal with more complex loop structures.
Stay tuned for the compilers lecture on how ML could be used to optimize the dataflow pattern for these cases.

## Slide 42: Squeezelerator: Hybrid WS/OS (Berkeley, Samsung)
Squeezelerator: Supports hybrid WS and OS data flow: up to 6x reduction in energy over OS, WS
  Determines execution flow statically based on trained weights (one time setup cost per network)
Output Stationary
Weight Stationary
Kwon, Kiseok, Alon Amid, Amir Gholami, Bichen Wu, Krste Asanovic, and Kurt Keutzer. "Co-design of deep neural nets and neural net accelerators for embedded vision applications." In 2018 55th ACM/ESDA/IEEE Design Automation Conference (DAC), pp. 1-6. IEEE, 2018.
Notes: Goal of WS: Reduce overhead of Weight read and write
Goal of OS: Reduce partial sum communication

## Slide 43: Squeezelerator: Hybrid OS/WS
Up to 6x Speedup relative to other architectures
Kwon, Kiseok, Alon Amid, Amir Gholami, Bichen Wu, Krste Asanovic, and Kurt Keutzer. "Co-design of deep neural nets and neural net accelerators for embedded vision applications." In 2018 55th ACM/ESDA/IEEE Design Automation Conference (DAC), pp. 1-6. IEEE, 2018.
Gholami A, Kwon K, Wu B, Tai Z, Yue X, Jin P, Zhao S, Keutzer K. Squeezenext: Hardware-aware neural network design. In Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition Workshops 2018 (pp. 1638-1647).
Notes: Squeezelerator achieves up to 2x and 6x speedup compared to reference OS and WS architectures, respectively.
Like other NN accelerators, Squeezelerator can achieve big (100x) over traditional architectures
Squeezelerator achieves up to 2x and 6x speedup compared to reference OS and WS accelerator architectures.
Squeezelator has the biggest impact on MobileNet, since MobileNet consist of two different layer types, which are favorable to OS and WS

## Slide 44: How to Evaluate HW Performance
FLOPs is not the same as wall clock time

## Slide 45: Williams Roofline Model
For decades programmers and architects did back-of-the-envelope calculations on compute vs communication at various levels of the memory hierarchy
  Processor to register file
  On-chip L1, L2 (L3?) caches
  Off-chip DRAM
  Interprocessor communication
UC Berkeley grad student Sam Williams gave a simple model, known as the Roofline Model, for reasoning about these issues
Williams, Samuel, Andrew Waterman, and David Patterson. Roofline: An insightful visual performance model for floating-point programs and multicore architectures. No. LBNL-2141E. Lawrence Berkeley National Lab.(LBNL), Berkeley, CA (United States), 2009.

## Slide 46: Roofline Model: y-axis
2
attainable Gflop/s
4
8
16
32
64
128
1
Peak flops
The y-axis describes the attained performance
It’s easy to add the “peak performance” as an upper bound

## Slide 47: Roofline Model: x-axis
2
1/8
Flops/Byte
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
1
The x-axis tells indicates for this particular application/kernel, for each floating-point operation (flop), how many bytes (B) must be fetched
For example if we have to fetch half precision floating-point numbers for each floating point operation, then:
1 FP16: 2 Bytes (16 bits)
2 FP16: 4 Bytes (32 bits)
1 FLOP requires 4 DRAM Bytes
Different applications/kernels,
not processors, move us along the X-axis
Kernel’s Arithmetic Intensity

## Slide 48: Bandwidth as Slope
2
1/8
FLOP/DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
1
Stream Bandwidth
Bandwidth is represented as a slope of
Peak Flops/ AI
It is a given by the system configuration/architecture
Remember m =
Example
m = y/x = 16
y
x =

## Slide 49: Bandwidth Meets Arithmetic Intensity
2
1/8
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
1
Peak flops
Stream Bandwidth
Kernel’s Arithmetic Intensity

## Slide 50: Designing an accelerator
1) Accelerators are Only the First 80% of the Problem
The other 80%: Full system design
The remaining 200%: SW development
2) HW design shouldn’t be about what can be built, rather what can be programmed
Stay tuned for the Lecture on AI Frameworks
3) Deploy at scale? Stay tuned for the next two lectures on scaling training
HW Definition Languages Co-Design Methodology Datacenter / Design, Deployment Datacenter / Heterogeneity
Research Challenges (if you are interested definition checkout EE 290 course by Prof. Shao) Abstraction Levels, DSLs Coarse Grained vs Fine Grain Acceleration Programming Languages, Programming Models Optimization Techniques, Runtimes
Naveen Kumar (Google)

## Slide 51: What Does the Future Look Like?

## Slide 52: The right dataflow, precision, and many other parameters heavily depend on the workload. If you were to design a HW today, it would at least take ~2years for its tape out, with a cost of ~$500M (estimate for 3nm) It must remain relevant through ~5 years to justify the huge upfront investment
What do you think is the right workload for the future to bet on?

## Slide 53: Next week’s readings

## Slide 54: Reading for Next Week
Mixed precision training. ICLR’18
  Discusses reduced precision training with IEEE FP16.
Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks [SIGRAPH’16]
  Discusses impact of dataflow on AI Hardware performance, introduces a new dataflow called row stationary
Interstellar: Using Halide’s Scheduling Language to Analyze DNN Accelerators (formerly: DNN Dataflow Choice Is Overrated) [ASPLOS’20]
  Studies the impact of different dataflow patterns
Gemmini: Enabling Systematic Deep-Learning Architecture Evaluation via Full-Stack Integration [DAC’21 [Best Paper Award]]
  Introduces an AI accelerator designed by UC Berkeley team with superior performance even compared to SOTA HW used in industry

## Slide 55: Extra Suggested Reading
Roofline: An Insightful Visual Performance Model for Floating-Point Programs and Multicore Architectures [CACM’08]
  Introduces a very simple method to evaluate/understand HW performance
A new golden age for computer architecture [CACM’19]
  Prof. Patterson and Prof. Hennessy’s great article on the motivations and opportunities for Domain Specific Accelerators
In-Datacenter Performance Analysis of a Tensor Processing Unit [ISCA’17]
  Design choices and performance analysis of TPU